## Slide 1: Modeling discussion
June 18, 2021

## Slide 2: Efforts that will be needed
8760-hour data for both RESOLVE (CAISO) and SWITCH (WECC).
Software for creation of input files to RESOLVE
Variable timesteps for RESOLVE
Other modifications?

## Slide 3: 1. 8760 data – note: these can be done now
Collection of data we can use for 8760-hour or at least 365-day simulations. This will be useful for both RESOLVE (CAISO, NW, SW,?) and SWITCH (WECC).
For RESOLVE:
  Create 8760 data sets for 2015, 2016, 2017, 2018, 2019, and 2020
  Use CAISO 5-min data to obtain hourly profiles for load, solar, wind to define CAISO values for existing (ignore the fact that solar was installed throughout the year)
  Adjust load – need to develop method for doing this (for EV, population changes…)
  For candidate resources:
    Locate good resources for each load zone (can use RSP candidate locations)
    Calculate 8760 for 2015-2020 for solar using SAM or PVWATTS (use current RESOLVE locations)
    Similarly, for wind using NREL Wind toolkit; Use the 107,000 data (for California) set to identify candidate resources; compare those locations to RESOLVE candidate resources. Look for winter-peaking resources
  What about other inputs?– determine strategy for defining Hydro limits What makes sense?
For SWITCH:
  Which years ? How many years? How do we select the desired years?
  Load is already extrapolated based on 20?? (extrapolation already exists – ignore weather)
  Candidate resources
    Use existing sites?
    Calculate 8760 for selected years for solar using SAM or PVWATTS (use identified sites)
    Calculate for wind using NREL Wind toolkit;. (use identified sites)

## Slide 4: 2. Create input files to RESOLVE and plot results
The “Scenario Tool” we have been using will not handle the 8760 data.
  Pedro wrote some Python code to modify the shapes.tab file.
  Write code that will create files in the new format using our 8760 data as input
  Select the year to pull the data from
  Apply a filter to select the timepoints we want to use
  Aggregate the data by timepoint
  E3 plans a Scenario tool that will create the files that have static input
  This part can be done now
We may need to build on the plotting files to use the new output file format (can be done as soon as we see the file output format)

## Slide 5: 3. Variable timesteps in RESOLVE
We should modify RESOLVE to be able to do time steps of longer than 1-hour steps (this already exists in SWITCH)
Make the time step variable and determined by the input file
Aggregate not use “snap shot” for this
Make a list of the changes – See later slide
Divide up the list and make the changes after E3 gives a stable version

## Slide 6: Other modifications
Solar thermal with storage done well in RESOLVE. Already in SWITCH – How does SWITCH handle this?
“Warm start” to RESOLVE
Model hybrid resources – can we define this easily?
Add capability to sell hydrogen
Add capability to monetize thermal energy
Add new storage resources

## Slide 7: Other input reviews
Review build limits for each resource – compare between SWITCH and RESOLVE
Review cost models

## Slide 8: Change: hourly costs
Adding the time step (in hours) to:
  timepoint_weight = (
  model.day_weight[model.day[tmp]] * model.discount_factor[model.period[tmp]]
  )
Should fix:
  # ### Hourly costs ### #
  variable_costs = float()
  fuel_costs = float()
  unit_start_costs = float()
  unit_shutdown_costs = float()
  unserved_energy_costs = float()
  overgen_costs = float()
  scheduled_curtailment_costs = float()
  upward_reg_violation_costs = float()
  downward_reg_violation_costs = float()
  upward_lf_reserve_violation_costs = float()
  downward_lf_reserve_violation_costs = float()
  spin_violation_costs = float()
  hurdle_rate_costs = float()

## Slide 9: Change: track energy in storage
  def storage_energy_tracking_rule(model, storage_resource, timepoint):
It may be that this can be adjusted in the final line:
  return (
  model.Energy_in_Storage_MWh[storage_resource, model.next_timepoint[timepoint]]
  == model.Energy_in_Storage_MWh[storage_resource, timepoint]
  + charging_mwh * model.charging_efficiency[model.technology[storage_resource]]
  - discharging_mwh
  / model.discharging_efficiency[model.technology[storage_resource]]
  )

## Slide 10: Other changes
Ancillary services
Ramp rate limits
Minimum shut down times; minimum on times
Track idle losses