## Slide 1
Modeling of Long Duration Storage for Decarbonization of California Energy System
EPC-19-060 - UC Merced
CPR #2 January 21, 2022

## Slide 2
Agenda
Introductions (5 min)
Project Overview & Status (30 min)
  Project Timeline
  How the project will inform current and future energy storage goals
  Results from the 2nd Workshop to present proposed scenarios for the preliminary analysis
  Objective of the preliminary analysis
  Preparation of data and modeling capabilities to meet the objective
Project Approach (25 min)
  Approach to conducting the preliminary analysis
  How the final analysis will differ from the preliminary analysis
  How the project team is engaging with stakeholders to produce meaningful and useful results
Questions (30+ min)
CPR Determination February 11, 2022

## Slide 3: Introduction to research team
        University of California Merced
        Sarah Kurtz
      University of
      California Berkeley
      Dan Kammen
      Sergio Castellanos
        University of California San Diego
        Patricia Hidalgo-Gonzalez
      University of North Carolina Chapel Hill
      Noah Kittner
Not all students are pictured

## Slide 4
PROJECT SCHEDULE
Technology Evaluation Team
Modeling Team
Baseline definition
Technology assessment
Scenario analysis

## Slide 5
PROJECT SCHEDULE
Task 3:
Technology Evaluation
Draft reports completed
Task 4:
Grid scenario selection
Primary discussion today
Task 5:
Final scenario analysis
Describe expected outcomes

## Slide 6
HOW THE PROJECT INFORMS CURRENT STORAGE GOALS
Exploratory studies do not give final answers, but give good guidance
Following slides provide findings we hope will be useful

## Slide 7
How the project informs storage goals – generation mix
Storage goals will depend on generation mix
  A roadmap for growth of wind and solar will provide a foundation for plan for storage
  Identify “flavors” of wind and solar as well as investments in transmission
  Solar provides more emphasis on frequently used diurnal storage
  Wind may provide more emphasis on infrequently used multi-day storage

## Slide 8
Data as basis of our recommendations
Curves assume perfect transmission within CAISO
(more study is planned)
Solar more clearly differentiates applications
Wind has less above the top line (“diurnal”) and more between the two lines (“cross-day”)
Add a note about pumped hydro

## Slide 9
Conclusions from data – solar-powered grid
Solar emphasizes frequently used diurnal storage
Wind emphasizes less frequently used cross-day storage
Priorities for solar-powered grid
  Diurnal storage is well defined – get through the night
    Power needed: Storage should be capable of powering entire grid (about 50 GW today – will grow with EV and heat pump demand)
    Energy needed: Through the night (> 0.3 TWh may grow to 1 TWh) motivates new technology with longer life and lower cost
  Resilience and seasonal is best met by cross-sector storage
    Cost targets for dedicated storage that is cycled once per year is difficult
    A large storage and distribution system that is used for transportation, industrial applications, etc. may share with power sector at a relatively low cost

## Slide 10
Lifetime is a special challenge for frequently used storage
Storage that is cycled every day may wear out quickly

## Slide 11
Long-duration storage can increase lifetime
Lifetime measured by number of cycles could increase from 10 yrs to almost 30 yrs when duration increase from 1 hr to 10 hrs.
This is an attractive option for storage with small energy capex but fast degradation
Chart: Discharge Duration (Hr)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Technical Life (Year) | 11.039 | 11.8182 | 12.987 | 14.2857 | 15.9091 | 17.7922 | 19.8052 | 21.8182 | 24.2857 | 27.013
Uniform Assumption | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15

## Slide 12
Conclusions from data – added wind
Storage goals will depend on generation mix
  A roadmap for growth of wind and solar will be a foundation for plan for storage
  Identify “flavors” of wind and solar as well as investments in transmission
Priorities for wind-powered grid – combining wind and solar decreases stored kWh (still need similar capacity, but less electricity is stored. This means that cost needs to be lower, but efficiency is less important)
  Diurnal storage is poorly defined
    Storage should be capable of powering entire grid (about 50 GW)
    Useful to have about 0.05 TWh that could cycle every day with high efficiency (like solar)
    Need more (maybe 0.1 TWh) that will cycle 1X per 2 or 3 days
      Efficiency & lifetime are less important because a smaller fraction of electricity is cycled and the less frequent use can enable longer storage lifetime
    Need even more (maybe 0.4 TWh) that will cycle less frequently (3 to 50 X/y)
      The attributes of this storage are challenging – may be best to use cross-sector storage?
  Resilience and seasonal is best met by cross-sector storage
Storage for wind-driven systems may have more income from capacity value than from sales of kWhs

## Slide 13
Big need – robust diurnal storage for most days
Number of hours (duration) is difficult to pin down (may not be useful to pin it down – will depend on amount of short-duration storage):
  Need to install storage with power to meet peak load (50 GW and growing)
  Won’t require 50 GW for entire night, so to supply a 12-h night, may use a 6-h battery operated at half power for 12 hours.
  Consider using a mixture of 4-h batteries to meet peak and 12-h batteries for entire night vs using 6-h or 8-h batteries for entire night and saving 4-h batteries only for the most challenging nights.
Primary need currently is to derisk new technologies for frequent use (able to cycle every day without wearing out) at low cost
Technology should project pathway to meeting targets:
  Low cost, long life, and high efficiency to give low LCOS
  Scalable to meaningful size (0.1 TWh)

## Slide 14
Benefit of storage’s marginal capex energy cost varies with application
Diurnal applications are not so affected by the energy capex
Applications that cycle infrequently depend more on energy capex

## Slide 15
Many attributes should be considered
Jobs, environmental impact, etc.
Footprint may guide applications
Small footprints are needed for distributed systems (especially residential)

## Slide 16
Many attributes should be considered
Jobs, environmental impact, etc.
Footprint may guide applications
Small footprints are helpful when space is constrained even for large systems

## Slide 17
Many attributes should be considered
Jobs, environmental impact, etc.
Footprint may guide applications
When space isn’t constrained and footprint doesn’t matter, some storage may be able to reach larger energy ratings

## Slide 18
Second big need – cross-sector storage
All scenarios need seasonal storage – suggest cross-sector is best
  Identify energy for other energy sectors: Hydrogen, ammonia, syn gas, or ?
  Derisk and scale to low cost
    Start with electrolyzers that can use surplus electricity to provide hydrogen for a local application
    Consider projects that could power rail or other fuel-cell vehicles
    Goal is to be able to first use surplus electricity, then create a large flexible load that makes demand management a real part of the solution
  Develop infrastructure
    What to recommend here? Read the advice from SoCalGas and others

## Slide 19
Third need – less-frequently used storage
Need is highly dependent on generation mix and weather (needed for wind-rich scenarios)
  Is part of 50 GW of storage
  Use may be highly variable and difficult to predict – maybe 10 X/y (range down to 3 X/y)
Primary need currently is to derisk new technologies with very low cost (efficiency is less important, though idle losses must be low)
For solar-only scenarios, may use cross-sector storage for < 10(?) X/y and diurnal storage capability for > 10(?) X/y
Short peak
Diurnal storage
Seasonal
storage
Short-duration storage
Cross-sector
storage
Self-contained
Long-d. storage
Cross-day storage

## Slide 20
HOW THE PROJECT WILL INFORM FUTURE STORAGE GOALS
Completion of final scenario analysis will better define:
  Cost targets for each storage product (with defined efficiency, duration, and degradation)
  Expected usage of those storage products
  Timeline for needed storage deployment and cost targets
  Better understanding of effects of imports on need for storage
  Better understanding of effects of “flavor” of wind and solar resources
  Better understanding of role of hydrogen including trade-off between using more electrolyzers to reduce curtailment and desired high capacity factors for those electrolyzers

## Slide 21
Additional priorities/needs
Electrification of transportation is critical
  Charging structure is required
  Charging structure that results in charging at night will require more storage
  Charging structure that enables daytime charging will enable solar deployment
   Therefore, identifying strategies for daytime charging is critical
Identification of flexible loads
  Electrolyzers may end up being biggest flexible load
  Factories that can turn off or other (recall the ships that unplugged in the harbor)
  Data centers that shift calculations to other sites
  Electrification of seasonal industries
  What was the project that Paty mentioned?
Biogas, geothermal, and other renewable sources

## Slide 22
Agenda
Introductions (5 min)
Project Overview & Status (30 min)
  Project Timeline
  How the project will inform current and future energy storage goals
  Results from the 2nd Workshop to present proposed scenarios for the preliminary analysis
  Objective of the preliminary analysis
  Preparation of data and modeling capabilities to meet the objective
Project Approach (25 min)
  Approach to conducting the preliminary analysis
  How the final analysis will differ from the preliminary analysis
  How the project team is engaging with stakeholders to produce meaningful and useful results
Questions (30+ min)
CPR Determination February 11, 2022

## Slide 23: Public Input from 2nd workshop
Input can be found at: https://efiling.energy.ca.gov/Lists/DocketLog.aspx?docketnumber=20-MISC-01
Southern California Gas Company
Green Hydrogen Coalition
Form Energy
CESA (received by email)
Two key inputs:
  Define more about plan for hydrogen (following slides will include a response)
  Share results with E3 (coordination is ongoing – input may be shared with E3)

## Slide 24: Modeling approach
Will use both RESOLVE and SWITCH to compare results
  Define long-duration storage adoptions
RESOLVE key explorations:
  Generation mix (tilted/untilted solar; various wind additions; transmission)
  Assumptions about pumped hydro storage and hydrogen storage
  Other sensitivity analysis
SWITCH key explorations:
  Infrastructure and economic opportunities for California to leverage WECC resources to achieve 100% RE by 2045
  Impacts of varying transmission deployment WECC-wide
  Impacts of re-designing planning and operational reserves rules on capacity expansion and operation

## Slide 25: Modeling approach – define LDES adoption
Create baseline scenario then evaluate storage products
1. Define storage product:
• Efficiency
• Hours of duration
2. Create price target graphs for each by varying price to see when it is adopted (see right)
Market is “ripe”
Market not yet demanding LDES so price must be extra low
Market is maturing and competing technologies are lower in price
This sort of analysis can help companies align their product design with market entry timing

## Slide 26: Modeling approach – storage matrix
Market is “ripe”
Market not yet demanding LDES so price must be extra low
Market is maturing and competing technologies are lower in price
Efficiency | Duration (h) | Idle loss | Relevant technologies
80% | 8, 16, 32, sometimes 128 | About 0 | pumped hydro, gravity, flow battery
70% | 8, 16, 32, sometimes 128 | About 0 | geomechanical, flow battery, metal-air, exfoliated-metal, gravity
60% | 8, 16, 32, sometimes 128 | 1%/day | flow battery, metal-air, exfoliated-metal, compressed air, liquid air, thermal
50% | 8, 16, 32, sometimes 128 | 1%/day | thermal
Storage product description will be selected from this matrix.
A single cost is assigned, then varied to create the graph on the right; repeat

## Slide 27: Modeling approach - hydrogen
Generation of hydrogen
  Allow model to build and schedule electrolyzers to create new demand as a flexible load (this plays a similar role to storage even if H2 is used for transportation)
Storage and distribution of hydrogen
  Very complicated, so simplify it:
  Sell H2 for $2/kg (or $1/kg or $3/kg) when generated
  Buy H2 for $?/kg if want to generate electricity ($2/kg to $12/kg)
  This allows us to look at multiple storage/distribution scenarios by adding $x/kg according to desired scenario
Electricity from hydrogen
  Using fuel cells
    Cross sector
    Dedicated
  Using turbines

## Slide 28: Baseline definition
Baseline
  Define expected storage options for each evaluation
    Li Batteries
    Pumped hydro – include all known projects
    Hydrogen – enable build of electrolyzers and sell H2 for $2/kg
  Costs from NREL 2021 ATB
  Include electricity generation from hydrogen using either fuel cell or combustion
  Software adjusted to do 365-day modeling (will try to use multiple years)
  Add new solar/wind generation options (model can select or not)
Sensitivities
  No new pumped hydro – what difference would this make?
  Different hydrogen prices (selling and buying combinations)
  EV charging scenarios
  High geothermal
  Natural gas with Allam cycle and carbon sequestration
Short peak
Diurnal storage
Seasonal
storage
Short-duration storage
Cross-sector
storage
Self-contained
Long-d. storage
Cross-day storage

## Slide 29: Software strategy for RESOLVE
Use new software that E3 is developing
Use ability to do full 8760 hours/year
Add ability to use variable time steps to hit most challenging hours
Use two-step approach to do capacity expansion plan followed by hourly dispatch
Add ability to select electrolyzers and monetize hydrogen generated
Include new pumped hydro storage as baseline (then explore effects of removing it)
Add new storage to see if adopted, then repeat with lower cost

## Slide 30: Status
Exploratory analysis has been very fruitful
  5 documents published
  4 documents under review
  2 documents being written
  2 oral presentations at virtual conferences; 5 posters presented by students
  Additional oral presentations
Currently transitioning from exploratory analysis to final analysis
E3 made first release of RESOLVE on Jan. 9, 2022
Have begun developing inputs and software modifications to RESOLVE
Have begun second round of studies using SWITCH
Expenditure rate was slowed while waiting for RESOLVE development; request a NCE to be able to fully explore modifications to RESOLVE

## Slide 31
Agenda
Introductions (5 min)
Project Overview & Status (30 min)
  Project Timeline
  How the project will inform current and future energy storage goals
  Results from the 2nd Workshop to present proposed scenarios for the preliminary analysis
  Objective of the preliminary analysis
  Preparation of data and modeling capabilities to meet the objective
Project Approach (25 min)
  Approach to conducting the preliminary analysis
  How the final analysis will differ from the preliminary analysis
  How the project team is engaging with stakeholders to produce meaningful and useful results
Questions (30+ min)
CPR Determination February 11, 2022

## Slide 32
Preliminary analysis vs Final analysis
Preliminary analysis will
  Optimize the approach for analyzing 365-day scenarios to enable hundreds of calculations while still retaining accuracy
  Identify the most interesting storage products to study
  Compare results from RESOLVE
Final analysis will
  Explore effects of each of the sensitivities (including any new options that are identified)
  Goal is to be able to quickly complete calculation for many scenarios in order to better assess confidence

## Slide 33: Engagement with stakeholders
Publications/presentations
  5 documents published
  4 documents under review
  2 documents being written
  2 oral presentations at virtual conferences; 5 posters presented
  Expert briefing organized by CCST “Technologies for Renewable Energy Storage”
  Assembly Select Committee on California’s Clean Energy Economy hearing (Chair Quirk)
  Panel discussion participation at Energy Storage North America (Long Beach)
  Presentation at UC Davis
Two draft reports posted for public comment and engagement with those who responded
Have invited guest speakers and shared our results in about ten meetings/year
TAC includes CAISO, CESA, Gridlab, LDES Assoc. of CA, NREL, TURN

## Slide 34: Engagement with stakeholders
  Antora Energy
  Augwind
  Bakersfield College
  Blue Marble
  Cat Creek
  CCST
  Disigno
  E3
  EDF
  Energy Vault
  ETES
  Form Energy
  GE Renewables
  GKN
  Gridlab
  Gridworks
  H2B2
  Harvard University
  Heliogen
  Highview Power
  Hydrostor
  Invinity
  Lawrence Berkeley Natl Lab
  Lawrence Livermore Natl Lab
  Malta, Inc
  NREL
  Quidnet
  Plus Energy Storage
  Reascend
  Renewell
  Rondo Energy
  SGRE COG IS EST TE SI (Siemens)
  Sinton Instruments
  Solar Turbines
  Strategen
  TURN
  UC Irvine
  Xcel Energy
  Zinc8 Energy
Have met with many organizations including:
As our results from the final scenario analysis become available, we plan to meet with the companies again to discuss the implications for them and identify whether additional calculations would be useful

## Slide 35
Agenda
Introductions (5 min)
Project Overview & Status (30 min)
  Project Timeline
  How the project will inform current and future energy storage goals
  Results from the 2nd Workshop to present proposed scenarios for the preliminary analysis
  Objective of the preliminary analysis
  Preparation of data and modeling capabilities to meet the objective
Project Approach (25 min)
  Approach to conducting the preliminary analysis
  How the final analysis will differ from the preliminary analysis
  How the project team is engaging with stakeholders to produce meaningful and useful results
Questions (30+ min)
CPR Determination February 11, 2022

## Slide 36: Discussion